## Slide 1: EEE 2113 Electrical Circuits Basic Concepts
Prepared by
Lec Saifur Rahman
Email: saifur@cse.uiu.ac.bd
Moblie: 01303529289

## Slide 2: Electric Circuit
An electric circuit is an interconnection of electrical elements

## Slide 3: Electrical Circuit
A real-life electrical circuit consists of various components

## Slide 4: System of Units

## Slide 5: Electrical Charge
Charge is an electrical property of the atomic particles of which matter consists, measured in coulombs (C).

## Slide 6: Electrical Charge
Atoms are made up of tiny particles called protons, neutrons, and electrons.
  Protons have a positive charge.
  Electrons have a negative charge.
  Neutrons have no charge.
Normally, an atom has the same number of protons and electrons, making it neutral.
  If an atom loses electrons, it becomes positively charged.
  If an atom gains electrons, it becomes negatively charged.
A single electron has a charge of -1.6 x C, while a single proton has a charge of + 1.6 x C

## Slide 7: Electrical Charge
The coulomb is a large unit for charges. In 1 C of charge, there are 6.24 x electrons. Thus, realistic or laboratory values of charges are on the order of pC, nC.
The Law of conservation of charge: states that a charge can neither be created nor destroyed, only transferred. Thus, the algebraic sum of the electric charges in a system does not change

## Slide 8: Flow of Charges
In electrical circuits, we are concerned with the charges that can freely move or flow
When we apply an electromotive force (emf) on charges, they gain energy, and start moving
  Emf is also known as voltage or potential difference
Notes: Direction of flow of current vs flow of electrons is opposite. We follow conventional direction of current.

## Slide 9: Electric Current
Electric current is the time rate of change of charge, measured in amperes (A).
Mathematically, the relationship between current i, charge q, and time t is
where current is measured in amperes (A), and 1 A = 1C/s

## Slide 10: Quantifying Electrical Charge
Notes: Charge and current not constant and can change with time. The classic physics formula we studied comes if we consider current to be constant.

## Slide 12
Math Problem Practice:

## Slide 14
Math Problem Practice:

## Slide 15: Voltage
To move the electron in a conductor in a particular direction requires some work or energy transfer.
This work is performed by an external electromotive force (emf), typically represented by the battery.
The voltage between two points a and b in an electric circuit is the energy (or work) needed to move a unit charge from a to b

## Slide 16: Voltage
Voltage (or potential difference) is the energy required to move a unit charge through an element, measured in volts (V).
1 V = 1 J/C

## Slide 17: Polarity of voltage
Voltage arises due to the difference in electric potential between two points in a circuit.
The point which has a higher potential is given a ‘+’ polarity, while the point which is at a lower potential is given a ‘-’ polarity
vab = -vba

## Slide 18: Electrical Power and Energy

## Slide 19: Sign Convention for Power
If current is entering through the positive terminal of a component, we give it a positive sign
A positive power indicates power absorbed by the component
If current is entering through the negative terminal of a component, we give it a negative sign
A negative power indicates power supplied by the component
In an electric circuit,
total power supplied = -total power absorbed
Notes: Show a basic circuit

## Slide 20: Law of Conservation of Energy in Circuits

## Slide 21
Math Problem Practice:

## Slide 22
Math Problem Practice:
Ans:

## Slide 23
Math Problem Practice:
Ans:

## Slide 24
Math Problem Practice: